## Slide 1: Let’s look at a normal lw instruction first…

## Slide 2
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
Opcode | Source register | Destination register | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
$6  Memory[8 + contents of $7]
PC value: 100010
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010

## Slide 3
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100010
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
This sequence of 1s and 0s
Opcode | Source register | Destination register | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
$6  Memory[8 + contents of $7]

## Slide 4
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100010100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 1, State 0: Fetch load instruction
IR  Memory(PC) || PC  PC + 4
IR contains: 100011-00111-00110-0000000000001000
0
01
See control logic discussion
00

## Slide 5
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 2, State 1: Decode instruction
A  RF[25:21] || B  RF[20:16] || ALUOut  PC + SignExt(IR[15:0])
00111
1000010
Load 1000010 into A register

## Slide 6
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 2, State 1: Decode instruction
A  RF[25:21] || B  RF[20:16] || ALUOut  PC + SignExt(IR[15:0])
00110
910
Load 910 into B register

## Slide 7
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 2, State 1: Decode instruction
A  RF[25:21] || B  RF[20:16] || ALUOut  PC + SignExt(IR[15:0])
Calculate address in case it is needed.
(hardware is available, so use ASAP)

## Slide 8
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 2, State 1: Decode instruction
A  RF[25:21] || B  RF[20:16] || ALUOut  PC + SignExt(IR[15:0])
0
11
See control logic discussion

## Slide 9
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 3, State 2 Calculate address
ALUOut  A + SignExt(IR[15:0])
1000010
‘A’ register is: 1000010
Immediate value is: 810 (0000 0000 0000 10002)
Immediate value is padded with leading 0s to get 2nd 32-bit number
  0000 0000 0000 0000 0000 0000 0000 10002
810

## Slide 10
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
1
10
See control logic discussion
Cycle 3, State 2: Calculate address
ALUOut  A + SignExt(IR[15:0])
1000010
810
1000810
ALUOut contains address to send to memory

## Slide 11
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 4, State 3: Get data from memory
MDR  Memory[ALUOut]
Address 1000810 sent to memory
Want to load 7010 into Memory Data Register
1000810
1000810
Data from memory is 7010

## Slide 12
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 4, State 3: Get data from memory
MDR  Memory[ALUOut]
1
Choose ALUOut to get memory address
Put 7010 in MDR

## Slide 13
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 5, State 4: Write data from memory to the register file
RF[IR(20:16)]  MDR
7010
00110

## Slide 14
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 5, State 4: Write data from memory to the register file
RF[IR(20:16)]  MDR
0
1
610
610
7010
7010

## Slide 15
Register file | 
address | content
6 (00110) | 910  7010
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 5, State 4: Write data from memory to the register file
RF[IR(20:16)]  MDR
0
1
610
610
7010
7010

## Slide 16: Now, let’s revisit lw++

## Slide 17: Recall…
lw++ would do the following…
  lw++ $6, 8($7)
    $6  Memory[8 + content of $7] ||
    $7  $7 + 4
Why is this useful?
  Assume we wanted to iterate through an array … we might use the following sequence of instructions:
    lw $t, 0($x)
    addi $x, $x, 4
  The above 2 instruction sequence (requiring 9 CCs) could be replaced by a single instruction that takes 5 or 6 CCs
Now, let’s talk about the hardware to make lw++ work!

## Slide 18
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
Opcode | Source register | Destination register | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
111111 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw++ $6,8($7)
$6  Memory[8 + contents of $7]
$7  $7 + 4
PC value: 100010
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode must change!
(Assume 111111 is available.)

## Slide 19
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100010
This sequence of 1s and 0s
Opcode | Source register | Destination register | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
111111 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw++ $6,8($7)
$6  Memory[8 + contents of $7]
$7  $7 + 4
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010

## Slide 20
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100010100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw++ $6,8($7)
Cycle 1, State 0: Fetch load instruction
IR  Memory(PC) || PC  PC + 4
IR contains: 111111-00111-00110-0000000000001000
0
01
See control logic discussion
00
Same as normal lw
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010

## Slide 21
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw++ $6,8($7)
Cycle 2, State 1: Decode instruction
A  RF[25:21] || B  RF[20:16] || ALUOut  PC + SignExt(IR[15:0])
00111
1000010
Load 1000010 into A register
Same as normal lw
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010

## Slide 22
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw++ $6,8($7)
Cycle 2, State 1: Decode instruction
A  RF[25:21] || B  RF[20:16] || ALUOut  PC + SignExt(IR[15:0])
00110
910
Load 910 into B register
Same as normal lw
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010

## Slide 23
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw++ $6,8($7)
Cycle 2, State 1: Decode instruction
A  RF[25:21] || B  RF[20:16] || ALUOut  PC + SignExt(IR[15:0])
Calculate address in case it is needed.
(hardware is available, so use ASAP)
Same as normal lw
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010

## Slide 24
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw++ $6,8($7)
Cycle 3, State 2 Calculate address
ALUOut  A + SignExt(IR[15:0])
1000010
A register is: 1000010
Immediate value is: 810 (0000 0000 0000 10002)
Immediate value is padded with leading 0s to get 2nd 32-bit number
  0000 0000 0000 0000 0000 0000 0000 10002
810
1000810
Same as normal lw
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010

## Slide 25
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
Cycle 4, State 3: Get data from memory
MDR  Memory[ALUOut]
Address 1000810 sent to memory
Want to load 7010 into Memory Data Register
1000810
1000810
Data from memory is 7010
address 100010: lw++ $6,8($7)
Part 1:
Same as normal lw
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010

## Slide 26
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
Cycle 4, State 3: Get data from memory
MDR  Memory[ALUOut] || ALUOut  [A] + 4
address 100010: lw++ $6,8($7)
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Part 2:
NEW!
1000010
810
Content of A and B registers still has not changed
Idea:
Use idle ALU to update the value in register A (i.e. $7) while the memory access occurs.

## Slide 27
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
Cycle 4, State 3: Get data from memory
MDR  Memory[ALUOut] || ALUOut  [A] + 4
address 100010: lw++ $6,8($7)
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Part 2:
NEW!
To make this work, need to assert other control signals in State 3 to do an add operation:
ALUSrcA = 1 # select A input
ALUSrcB = 01 # select 4 input
ALUOp = 00 # perform add
MemRead
IorD = 1
ALUSrcA = 1
ALUSrcB = 01
ALUOp = 00
3
New state would look like…

## Slide 28
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
Cycle 4, State 3: Get data from memory
MDR  Memory[ALUOut] || ALUOut  [A] + 4
address 100010: lw++ $6,8($7)
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Part 2:
NEW!
1
1000010
See control logic discussion
do add
01
1000410
ALUOut contains 1000410

## Slide 29: Now, to finish, we need to support the write back of both the MDR register AND the ALUOut register
For dramatic effect, let’s continue on another slide…

## Slide 30: Option A: Write back MDR and ALUOut in the same CC…

## Slide 31
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
Cycle 5, State 12: Write data back…
RF[IR(20-16)]  MDR || RF[IR(25:21)]  ALUOut
address 100010: lw++ $6,8($7)
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Option A
Aw, snap!
With existing datapath, only 1 register can be written at a time…

## Slide 32: Option A: Write back MDR and ALUOut in the same CC…
Solution:
Add register file hardware
Update the FSM
Let’s update the register file hardware 1st…

## Slide 33
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
Cycle 5, State 12: Write data back…
RF[IR(20-16)]  MDR || RF[IR(25:21)]  ALUOut
address 100010: lw++ $6,8($7)
Option A
Can keep existing hardware the same, but need to add:
Another address port
  “Write register 2”
Another data port
  “Write data 2”
Another control signal
  RegWrite2
IR(25:21) – i.e. 001112
Input to
Write Register 2
ALUOut
(1000410)
Input to
Write Data 2
New control signal:
RegWrite2

## Slide 34: New FSM diagram is thus:
RegDst = 0
RegWrite
MemtoReg = 1
RegWrite2
12
lw++
Need a new state because we want to do different things for lw and lw ++

## Slide 35: Option B: Write back MDR and ALUOut in the different CCs…

## Slide 36
Register file | 
address | content
6 (00110) | 910  7010
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
Cycle 5, State 4: Write data from memory to the register file
RF[IR(20:16)]  MDR
0
1
610
610
7010
7010
address 100010: lw++ $6,8($7)
Same as normal lw

## Slide 37
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
Cycle 5, State 13: Write data from ALUOut to the register file
RF[IR(25:21)]  ALUOut
address 100010: lw++ $6,8($7)
Aw, snap!
No path for bits 25:21 of IR to use as write address…
To fix:
Add another input to mux
Now need 2 control signals instead of 1
00
01
10
IR(20:16)
IR(15:11)
IR(25:21)

## Slide 38: New FSM diagram is thus:
RegDst = 10
RegWrite
MemtoReg = 0
13
lw++
Notes:
RegDst = 10
  Selects IR(25:21)
RegWrite
  Enables register file to be written
MemtoReg = 0
  Selects ALUOut as input to the register file