## Slide 1: Lecture 15: Midterm Review
Copyright © 2007 Frank Vahid
Instructors of courses requiring Vahid's Digital Design textbook (published by John Wiley and Sons) have permission to modify and use these slides for customary course-related activities, subject to keeping this copyright notice in place and unmodified. These slides may be posted as unanimated pdf versions on publicly-accessible course websites.. PowerPoint source (or pdf with animations) may not be posted to publicly-accessible websites, but may be posted for students on internal protected sites or distributed directly to students by other electronic means. Instructors may make printouts of the slides available to students for a reasonable photocopying charge, without incurring royalties. Any other use requires explicit permission. Instructors may obtain PowerPoint source or obtain special use permissions from Wiley – see http://www.ddvahid.com for information.
Some slides/images from Vahid text – hence this notice:

## Slide 2: Board discussion summary:
for i=0; i<5; i++ {
a = (a*b) + c;
}
A hypothetical translation:
MULT temp,a,b # temp  a*b
MULT r1,r2,r3 # r1  r2*r3
ADD a,temp,c # a  temp+c
ADD r2,r1,r4 # r2  r1+r4
Can define codes for MULT and ADD
Assume MULT = 110011 & ADD = 001110
stored program becomes
PC | 110011 | 000001 | 000010 | 000011
PC+1 | 001110 | 000010 | 000001 | 000100

## Slide 3: Datapath + control =
Instruction Set – List of allowable instructions and their representation in memory, e.g.,
  Load instruction—0000 r3r2r1r0 d7d6d5d4d3d2d1d0
  Store instruction—0001 r3r2r1r0 d7d6d5d4d3d2d1d0
  Add instruction— 0010 ra3ra2ra1ra0 rb3rb2rb1rb0 rc3rc2rc1rc0
Instruction memory
I
0: 0000 0000 00000000
1: 0000 0001 00000001
2: 0010 0010 0000 0001
3: 0001 0010 00001001
0: RF[0]=D[0]
1: RF[1]=D[1]
2: RF[2]=RF[0]+RF[1]
3: D[9]=RF[2]
Desired program
operands
Instructions in 0s and 1s – machine code
opcode
“Instruction” is an idea that
helps abstract 1s, 0s, but
still provides info. about HW
What does this tell you
about data memory?
What does this tell us about
the register file?
3-instruction
programmable processor

## Slide 4: Basic datapath operations
Load: load data from data memory to RF
ALU operation: transforms data by passing one or two RF values through ALU (for ADD, SUB, AND, OR, etc.); data written back to RF
Store operation: stores RF register value back into data memory
Each operation can be done in one clock cycle
Register file RF
Data memory D
ALU
n-bit
2x
1
Register file RF
Data memory D
ALU
n-bit
2x
1
Register file RF
Data memory D
ALU
n-bit
2x
1
Load operation
ALU operation
Store operation

## Slide 5: The datapath control unit
D[9] = D[0] + D[1] – requires a sequence of four datapath operations:
      0: RF[0] = D[0]
      1: RF[1] = D[1]
      2: RF[2] = RF[0] + RF[1]
      3: D[9] = RF[2]
Each operation is an instruction
  Sequence of instructions – program
  Programmable processors decomposing desired computations into processor-supported operations
  Store program in instruction memory
  Control unit reads each instruction and executes it on the datapath
    PC: Program counter – address of current instruction
    IR: Instruction register – current instruction
Register file RF
Data memory D
ALU
n-bit
2
x
1
Datapath
0: RF[0]=D[0]
1: RF[1]=D[1]
2: RF[2]=RF[0]+RF[1]
3: D[9]=RF[2]
I
Control unit
Instruction memory
PC
IR
Controller
Foreshadowing:
What if we want ALU to add, subtract?
How do we tell it what to do?

## Slide 6: The datapath control unit
To carry out each instruction, the control unit must:
  Fetch – Read instruction from instruction memory
  Decode – Determine the operation and operands of the instruction
  Execute – Carry out the instruction's operation using the datapath
RF[0]=D[0]
0
->
1
R[0]: ??
 99
"load"
Instruction memory
I
Control unit
Controller
PC
I
R
0: RF[0]=D[0]
1: RF[1]=D[1]
2: RF[2]=RF[0]+RF[1]
3: D[9]=RF[2]
(
a
)
Fetch
RF[0]=D[0]
Instruction memory
I
Control unit
PC
I
R
0: RF[0]=D[0]
1: RF[1]=D[1]
2: RF[2]=RF[0]+RF[1]
3: D[9]=RF[2]
1
(
b
)
Controller
Decode
Register file RF
Data memory D
D[0]: 99
ALU
n-bit
2
x
1
Datapath
Instruction memory
I
Control unit
Controller
PC
I
R
0: RF[0]=D[0]
1: RF[1]=D[1]
2: RF[2]=RF[0]+RF[1]
3: D[9]=RF[2]
RF[0]=D[0]
1
(
c
)
Execute

## Slide 7: Control signals must arrive at right time
To design the processor, we can begin with a high-level state machine description of the processor's behavior
  Control unit manages instruction fetch, flow through datapath HW
Decode
Fetch
Init
PC=0
IR=I[PC]
PC=PC+1
Load
RF[ra]=D[d]
op=0000
Store
Add
RF[ra] =
RF[rb]+
RF[rc]
D[d]=RF[ra]
op=0001
op=0010

## Slide 8: Control signals must arrive at right time
Convert high-level state machine description of entire processor to FSM description of controller
  Use datapath and other components to achieve same behavior
PC
clr
up
16
I
R
Id
16
16
I
data
rd
addr
Controller
Control unit
Datapath
RF_W_wr
RF_Rp_addr
RF_Rq_addr
RF_Rq_rd
RF_Rp_rd
RF_W_addr
D_addr 8
D_rd
D_wr
RF_s
alu_s0
addr
D
rd
wr
256
x
16
16
x
16
RF
16-bit
2
x
1
W_data
R_data
Rp_data
Rq_data
W_data
W_addr
W_wr
Rp_addr
Rp_rd
Rq_addr
Rq_rd
0
16
16
16
16
16
16
s
1
A
B
s0
ALU
4
4
4
Fetch
Decode
Init
PC=0
PC_ clr=1
Store
I
R=
I
[PC] PC=PC+1
I
_rd=1 PC_inc=1
I
R_ld=1
Load
Add
RF[ra] = RF[rb]+
RF[rc]
D[d]=RF[ra]
RF[ra]=D[d]
op=0000
op=0001
op=0010
D_addr=d
D_wr=1
RF_s=X
RF_Rp_addr=ra
RF_Rp_rd=1
RF_Rp_addr=rb
RF_Rp_rd=1
RF_s=0
RF_Rq_addr=rc
RF_Rq _rd=1
RF_W_addr=ra
RF_W_wr=1
alu_s0=1
D_addr=d
D_rd=1
RF_s=1
RF_W_addr=ra
RF_W_wr=1

## Slide 9: More complex state diagram
Fetch
Decode
Init
PC_clr=1
Store
I
_rd=1
PC_inc=1
I
R_ld=1
Load
Add
D_addr=d
D_wr=1
RF_s1
=
X
RF_s0
=
X
RF_Rp_addr=ra
RF_Rp_rd=1
RF_Rp_addr=rb
RF_Rp_rd=1
RF_s1
=
0
RF_s0
=
0
RF_Rq_add=rc
RF_Rq_rd=1
RF_W_addr_ra
RF_W_wr=1
alu_s1
=
0
alu_s0
=
1
D_addr=d
D_rd=1
RF_s1
=
0
R
F
_
s0
=
1
RF_W_addr=ra
RF_W_wr=1
Subtract
Load-
constant
Jump-if-zero
RF_Rp_addr=rb
RF_Rp_rd=1
RF_s1=0
RF_s0=0
RF_Rq_addr=rc
RF_Rq_rd=1
RF_W_addr=ra
RF_W_wr=1
alu_s1=1
alu_s0=0
RF_Rp_addr=ra
RF_Rp_rd=1
RF_s1=1
RF_s0=0
RF_W_addr=ra
RF_W_wr=1
Jump-if-
zero-jmp
PC_ld=1
op=0100
op=0101
op=0010
op=0011
op=0001
op=0000
RF_Rp_zero
RF_Rp_zero'
State diagram tells you how many CCs instruction takes; what control signals must be generated in each state

## Slide 10: Be sure you understand the timing!
Q1: D[8] = D[8] + RF[1] + RF[4]
…
I[15]: Add R2, R1, R4 RF[1] = 4
I[16]: MOV R3, 8 RF[4] = 5
I[17]: Add R2, R2, R3 D[8] = 7
…
(n+1)
Fetch
PC=15
IR=xxxx
(n+2)
Decode
PC=16
IR=2214h
(n+3)
Execute
PC=16
IR=2214h
RF[2]=
xxxxh
(n+4)
Fetch
PC=16
IR=2214h
RF[2]=
0009h
(n+5)
Decode
PC=17
IR=0308h
(n+6)
Execute
PC=17
IR=0308h
RF[3]=
xxxxh
CLK
(n+7)
Fetch
PC=17
IR=0308h
RF[3]=
0007h

## Slide 11: Common (and good) performance metrics
latency: response time, execution time
  good metric for fixed amount of work (minimize time)
throughput: work per unit time
  = (1 / latency) when there is NO OVERLAP
  > (1 / latency) when there is overlap
    in real processors there is always overlap
  good metric for fixed amount of time (maximize work)
comparing performance
  A is N times faster than B if and only if:
    time(B)/time(A) = N
  A is X% faster than B if and only if:
    time(B)/time(A) = 1 + X/100
10 time units
Finish
each
time unit

## Slide 12: CPU time: the “best” metric
Instruction
Count
Clock Cycle
Time
We can see CPU performance dependent on:
  Clock rate, CPI, and instruction count
CPU time is directly proportional to all 3:
  Therefore an x % improvement in any one variable leads to an x % improvement in CPU performance
But, everything usually affects everything:
Hardware
Technology
CPI
Organization
ISAs
Compiler Technology

## Slide 13: Encoding complexity may vary, but same general operations performed…
MIPS processor:
  Assembly: add $9, $7, $8 # add rd, rs, rt: RF[rd] = RF[rs]+RF[rt]
  (add: op+func)
  Machine:
op (6)
rs (5)
rt (5)
rd (5)
shamt (5)
31 26 25 21 20 16 15 11 10 6 5 0
funct (6)
B: 000000 00111 01000 01001 xxxxx 100000
D: 0 7 8 9 x 32
6-instruction processor:
Add instruction: 0010 ra3ra2ra1ra0 rb3rb2rb1rb0 rc3rc2rc1rc0
Add Ra, Rb, Rc—specifies the operation RF[a]=RF[b] + RF[c]

## Slide 14
More complex instruction encodings, same general flow through the datapath…
Path of Add from start to finish.

## Slide 15: Review: MIPS R-Type
R-type: All operands are in registers
  Assembly: add $9, $7, $8 # add rd, rs, rt: RF[rd] = RF[rs]+RF[rt]
  (add: op+func)
  Machine:
B: 000000 00111 01000 01001 xxxxx 100000
D: 0 7 8 9 x 32
op (6)
rs (5)
rt (5)
rd (5)
shamt (5)
31 26 25 21 20 16 15 11 10 6 5 0
funct (6)

## Slide 16: Review: MIPS I-Type (arithmetic)
I-type: One operand is an immediate value and others
are in registers
Example: addi $s2, $s1, 128 # addi rt, rs, Imm
# RF[18] = RF[17]+128
Op (6)
rs (5)
rt (5)
Address/Immediate value (16)
31 26 25 21 20 16 15 0
B: 001000 10001 10010 0000000010000000
D: 8 17 18 128

## Slide 17: Review: MIPS I-Type (load/store)
I-type: One operand is an immediate value and others
are in registers
Example: lw $s3, 32($t0) # RF[19] = Memory[RF[8]+32]
Op (6)
rs (5)
rt (5)
Address/Immediate value (16)
31 26 25 21 20 16 15 0
B: 100011 01000 10011 0000000000100000
D: 35 8 19 32

## Slide 18: Review: MIPS I-Type (branch)
I-type: One operand is an immediate value and others
are in registers
Example: Again: bne $t0, $t1, Again
# if (RF[8]!=RF[9]) PC=PC+4+Imm*4
# else PC=PC+4 (Why “4”?)
Op (6)
rs (5)
rt (5)
Address/Immediate value (16)
31 26 25 21 20 16 15 0
B: 00101 01000 01001 1111111111111111
D: 5 8 9 -1
PC-relative addressing

## Slide 19: MIPS Procedure Handling
The big picture:
    Caller Callee
Need “jump” and “return”:
  jal ProcAddr # issued in the caller
    jumps to ProcAddr
    save the return instruction address in $31
    PC = JumpAddr, RF[31]=PC+4;
  jr $31 ($ra) # last instruction in the callee
    jump back to the caller procedure
    PC = RF[31]
PC
PC+4
r0
r1
r31
b0
bn-1
...
...
0
PC
HI
LO
$31 = $ra (return address)
jal
jr

## Slide 20: MIPS register conventions
Name
R#
Usage
Preserved on Call
$zero
0
The constant value 0
n.a.
$v0-$v1
2-3
Values for results & expr. eval.
no
$a0-$a3
4-7
Arguments
no
$t0-$t7
8-15
Temporaries
no
$s0-$s7
16-23
Saved
yes
$t8-$t9
24-25
More temporaries
no
$gp
28
Global pointer
yes
$sp
29
Stack pointer
yes
$fp
30
Frame pointer
yes
$ra
31
Return address
yes
$at
1
Reserved for assembler
n.a.
$k0-$k1
26-27
Reserved for use by OS
n.a.
(and the “conventions” associated with them)

## Slide 21: Procedure call essentials: Good Strategy
Caller at call time
  put arguments in $a0..$a4
  save any caller-save temporaries
  jal ..., $ra
Callee at entry
  allocate all stack space
  save $ra, $fp + $s0..$s7 if necessary
Callee at exit
  restore $ra, $fp + $s0..$s7 if used
  deallocate all stack space
  put return value in $v0
Caller after return
  retrieve return value from $v0
  restore any caller-save temporaries
most of the work
do most work at callee entry/exit

## Slide 22: Use stack for nested procedure calls…
Each procedure is associated with a call frame
Each frame has a frame pointer: $fp ($30)
Argument 5 is in 0($fp)
$sp
$fp
Snap shots of stack
main
proc1
proc2
proc3
main {
…
proc1
…}
proc1 {
…
proc2
…}
proc2 {
… proc3
…}
Local
variables
Saved
Registes
($fp)
($ra)
…
Argument 6
Argument 5
Because $sp can change dynamically, often easier/intuitive to reference extra arguments via stable $fp – although can use $sp with a little extra math

## Slide 23: A Single Cycle Datapath

## Slide 24: Instruction execution (multi-cycle summary):
Step name
Action for R-type
instructions
Action for memory-reference
instructions
Action for
branches
Action for
jumps
Instruction fetch
IR = Mem[PC],
PC = PC + 4
Instruction
A =RF [IR[25:21]],
decode/register fetch
B = RF [IR[20:16]],
ALUOut = PC + (sign-extend (IR[1:-0]) << 2)
Execution, address
ALUOut = A op B
ALUOut = A + sign-extend
if (A =B) then
PC = PC [31:28] |
computation, branch/
(IR[15:0])
PC = ALUOut
(IR[25:0]<<2)
jump completion
Memory access or R-type
RF [IR[15:11]] =
Load: MDR = Mem[ALUOut]
completion
ALUOut
or
Store: Mem[ALUOut]= B
Memory read completion
Load: RF[IR[20:16]] = MDR

## Slide 25: FSM with Exception Handling

## Slide 26: Tracing the lw instruction…

## Slide 27
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
Opcode | Source register | Destination register | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
$6  Memory[8 + contents of $7]
PC value: 100010
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010

## Slide 28
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100010
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
This sequence of 1s and 0s
Opcode | Source register | Destination register | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
$6  Memory[8 + contents of $7]

## Slide 29
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100010100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 1, State 0: Fetch load instruction
IR  Memory(PC) || PC  PC + 4
IR contains: 100011-00111-00110-0000000000001000
0
01
See control logic discussion
00

## Slide 30
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 2, State 1: Decode instruction
A  RF[25:21] || B  RF[20:16] || ALUOut  PC + SignExt(IR[15:0])
00111
1000010
Load 1000010 into A register

## Slide 31
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 2, State 1: Decode instruction
A  RF[25:21] || B  RF[20:16] || ALUOut  PC + SignExt(IR[15:0])
00110
910
Load 910 into B register

## Slide 32
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 2, State 1: Decode instruction
A  RF[25:21] || B  RF[20:16] || ALUOut  PC + SignExt(IR[15:0])
Calculate address in case it is needed.
(hardware is available, so use ASAP)

## Slide 33
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 2, State 1: Decode instruction
A  RF[25:21] || B  RF[20:16] || ALUOut  PC + SignExt(IR[15:0])
0
11
See control logic discussion

## Slide 34
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 3, State 2 Calculate address
ALUOut  A + SignExt(IR[15:0])
1000010
‘A’ register is: 1000010
Immediate value is: 810 (0000 0000 0000 10002)
Immediate value is padded with leading 0s to get 2nd 32-bit number
  0000 0000 0000 0000 0000 0000 0000 10002
810

## Slide 35
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
1
10
See control logic discussion
Cycle 3, State 2: Calculate address
ALUOut  A + SignExt(IR[15:0])
1000010
810
1000810
ALUOut contains address to send to memory

## Slide 36
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 4, State 3: Get data from memory
MDR  Memory[ALUOut]
Address 1000810 sent to memory
Want to load 7010 into Memory Data Register
1000810
1000810
Data from memory is 7010

## Slide 37
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 4, State 3: Get data from memory
MDR  Memory[ALUOut]
1
Choose ALUOut to get memory address
Put 7010 in MDR

## Slide 38
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 5, State 4: Write data from memory to the register file
RF[IR(20:16)]  MDR
7010
00110

## Slide 39
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 5, State 4: Write data from memory to the register file
RF[IR(20:16)]  MDR
0
1
610
610
7010
7010

## Slide 40
Register file | 
address | content
6 (00110) | 910  7010
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw $6,8($7)
Cycle 5, State 4: Write data from memory to the register file
RF[IR(20:16)]  MDR
0
1
610
610
7010
7010

## Slide 41: Now, let’s revisit lw++

## Slide 42: Recall…
lw++ would do the following…
  lw++ $6, 8($7)
    $6  Memory[8 + content of $7] ||
    $7  $7 + 4
Why is this useful?
  Assume we wanted to iterate through an array … we might use the following sequence of instructions:
    lw $t, 0($x)
    addi $x, $x, 4
  The above 2 instruction sequence (requiring 9 CCs) could be replaced by a single instruction that takes 5 or 6 CCs
Now, let’s talk about the hardware to make lw++ work!

## Slide 43
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
Opcode | Source register | Destination register | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
111111 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw++ $6,8($7)
$6  Memory[8 + contents of $7]
$7  $7 + 4
PC value: 100010
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode must change!
(Assume 111111 is available.)

## Slide 44
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100010
This sequence of 1s and 0s
Opcode | Source register | Destination register | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
111111 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw++ $6,8($7)
$6  Memory[8 + contents of $7]
$7  $7 + 4
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010

## Slide 45
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100010100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw++ $6,8($7)
Cycle 1, State 0: Fetch load instruction
IR  Memory(PC) || PC  PC + 4
IR contains: 111111-00111-00110-0000000000001000
0
01
See control logic discussion
00
Same as normal lw
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010

## Slide 46
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw++ $6,8($7)
Cycle 2, State 1: Decode instruction
A  RF[25:21] || B  RF[20:16] || ALUOut  PC + SignExt(IR[15:0])
00111
1000010
Load 1000010 into A register
Same as normal lw
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010

## Slide 47
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw++ $6,8($7)
Cycle 2, State 1: Decode instruction
A  RF[25:21] || B  RF[20:16] || ALUOut  PC + SignExt(IR[15:0])
00110
910
Load 910 into B register
Same as normal lw
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010

## Slide 48
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw++ $6,8($7)
Cycle 2, State 1: Decode instruction
A  RF[25:21] || B  RF[20:16] || ALUOut  PC + SignExt(IR[15:0])
Calculate address in case it is needed.
(hardware is available, so use ASAP)
Same as normal lw
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010

## Slide 49
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
address 100010: lw++ $6,8($7)
Cycle 3, State 2 Calculate address
ALUOut  A + SignExt(IR[15:0])
1000010
A register is: 1000010
Immediate value is: 810 (0000 0000 0000 10002)
Immediate value is padded with leading 0s to get 2nd 32-bit number
  0000 0000 0000 0000 0000 0000 0000 10002
810
1000810
Same as normal lw
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010

## Slide 50
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
Cycle 4, State 3: Get data from memory
MDR  Memory[ALUOut]
Address 1000810 sent to memory
Want to load 7010 into Memory Data Register
1000810
1000810
Data from memory is 7010
address 100010: lw++ $6,8($7)
Part 1:
Same as normal lw
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010

## Slide 51
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
Cycle 4, State 3: Get data from memory
MDR  Memory[ALUOut] || ALUOut  [A] + 4
address 100010: lw++ $6,8($7)
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Part 2:
NEW!
1000010
810
Content of A and B registers still has not changed
Idea:
Use idle ALU to update the value in register A (i.e. $7) while the memory access occurs.

## Slide 52
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
Cycle 4, State 3: Get data from memory
MDR  Memory[ALUOut] || ALUOut  [A] + 4
address 100010: lw++ $6,8($7)
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Part 2:
NEW!
To make this work, need to assert other control signals in State 3 to do an add operation:
ALUSrcA = 1 # select A input
ALUSrcB = 01 # select 4 input
ALUOp = 00 # perform add
MemRead
IorD = 1
ALUSrcA = 1
ALUSrcB = 01
ALUOp = 00
3
New state would look like…

## Slide 53
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
Cycle 4, State 3: Get data from memory
MDR  Memory[ALUOut] || ALUOut  [A] + 4
address 100010: lw++ $6,8($7)
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Part 2:
NEW!
1
1000010
See control logic discussion
do add
01
1000410
ALUOut contains 1000410

## Slide 54: Now, to finish, we need to support the write back of both the MDR register AND the ALUOut register
For dramatic effect, let’s continue on another slide…

## Slide 55: Option A: Write back MDR and ALUOut in the same CC…

## Slide 56
Register file | 
address | content
6 (00110) | 910
7 (00111) | 1000010
PC value: 100410
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
Cycle 5, State 12: Write data back…
RF[IR(20-16)]  MDR || RF[IR(25:21)]  ALUOut
address 100010: lw++ $6,8($7)
Memory | 
address | content
100010 | lw++ encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Option A
Aw, snap!
With existing datapath, only 1 register can be written at a time…

## Slide 57: Option A: Write back MDR and ALUOut in the same CC…
Solution:
Add register file hardware
Update the FSM
Let’s update the register file hardware 1st…

## Slide 58
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
Cycle 5, State 12: Write data back…
RF[IR(20-16)]  MDR || RF[IR(25:21)]  ALUOut
address 100010: lw++ $6,8($7)
Option A
Can keep existing hardware the same, but need to add:
Another address port
  “Write register 2”
Another data port
  “Write data 2”
Another control signal
  RegWrite2
IR(25:21) – i.e. 001112
Input to
Write Register 2
ALUOut
(1000410)
Input to
Write Data 2
New control signal:
RegWrite2

## Slide 59: New FSM diagram is thus:
RegDst = 0
RegWrite
MemtoReg = 1
RegWrite2
12
lw++
Need a new state because we want to do different things for lw and lw ++

## Slide 60: Option B: Write back MDR and ALUOut in the different CCs…

## Slide 61
Register file | 
address | content
6 (00110) | 910  7010
7 (00111) | 1000010
PC value: 100410
Memory | 
address | content
100010 | lw encoding
… | …
1000010 | 5010
1000410 | 6010
1000810 | 7010
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
Cycle 5, State 4: Write data from memory to the register file
RF[IR(20:16)]  MDR
0
1
610
610
7010
7010
address 100010: lw++ $6,8($7)
Same as normal lw

## Slide 62
Opcode | Source | Destination | Immediate value
Bits 31-26 | Bits 25-21 | Bits 20-16 | Bits 15-0
100011 | 00111 | 00110 | 0000 0000 0000 1000
Cycle 6, State 13: Write data from ALUOut to the register file
RF[IR(25:21)]  ALUOut
address 100010: lw++ $6,8($7)
Aw, snap!
No path for bits 25:21 of IR to use as write address…
To fix:
Add another input to mux
Now need 2 control signals instead of 1
00
01
10
IR(20:16)
IR(15:11)
IR(25:21)

## Slide 63: New FSM diagram is thus:
RegDst = 10
RegWrite
MemtoReg = 0
13
lw++
Notes:
RegDst = 10
  Selects IR(25:21)
RegWrite
  Enables register file to be written
MemtoReg = 0
  Selects ALUOut as input to the register file