## Slide 1: Chapter 1 – Fluid Properties
CE30460 - Fluid Mechanics
Diogo Bolster

## Slide 2: What is a Fluid?
A substance that deforms continuously when acted on by a shearing stress
A solid will deform to a certain point for a given stress
Liquids and Gases are fluids (water, oil, air)
Some substances can act as solids and fluids (e.g. soil standing/ avalanche)

## Slide 3: What happens for a fluid/solid ?

## Slide 4: Units and Dimensions Important in Fluids
Primary Dimensions
    Length (L)
    Time (T)
    Mass (M)
    Temperature (Q)
For any relationship A=B
    Units (A)=Units (B) Dimensional Homogeneity
  Can this ever not be true?
Sometimes
Force/Time /Mass/Temperature
Notes: In class example on the board

## Slide 5: Systems of Units
British SI (Systeme International)
Foot (ft) Meter (m)
Second (s) Second (s)
Pound (lbf) Kilogram (kg) Slug (32.17 lbm)
Degree Rankine (oR) Degree Kelvin (oK) related to Fahrenheit related to Celsius (oF+459.67) (oC+273.15)
INSERT JOKE HERE
https://www.facebook.com/BillyKellyComedian/videos/2082094818558066/
Minute 3:50

## Slide 6: Why are Units so Important

## Slide 7: Sample Problem 1 – Unit Homogeneity
Consider the formula
F – force, v – velocity, t – time, l – length
What are the unites of the Ka, Kb and Kc terms?

## Slide 8: Fluid Mass and Weight
Density r [M L-3]
    Varies with temperature and pressure
        Liquid (often negligible changes)
        Gasses (can be very important to account for changes)
Specific Volume (inverse density) v [L3 M-1]
Specific Weight g=r g [What are the units?]
Specific gravity SG=r/rwater@4C (i.e. 1 for water at 4oC it equal to 1, for mercury 13.55, where the density of mercury would be 13550 kg m-3).

## Slide 9: Density Effects (called buoyancy) can be very very important in Environmental Flows
https://www.youtube.com/watch?v=AfueW-cp_s8
Example 1 – Thunderstorm Fronts
How quickly do you think it moves – make an educated guess? What matters?
Deduce it from there

## Slide 10: Density Effects – Saltwater Intrusion

## Slide 11: Sample Problem – Density
A volume of 1m^3 is occupied by two fluids. Fluid 1 has a specific gravity of SG=2, while Fluid 2 has a density of 800 kgm-3? There is three times as much mass of Fluid 2 as there is of Fluid 1.
How much mass is there of each fluid?
What volumetric fraction of the total volume does each fluid occupy?

## Slide 12: Ideal Gases
Gases are much more compressible than liquids and their density is sensitive to changes in pressure and temperature. An ideal gas is one which follows the ideal gas law:
R – the gas constant depends on the particular gas in question.
https://ch301.cm.utexas.edu/simulations/js/idealgaslaw/
Pressure is a relative measurements and two common used measures in engineering are : Gauge vs. Absolute pressure (here we must use absolute)
    Absolute is relative to absolute zero pressure
    Gauge is measured relative to atmospheric (i.e. Absolute-Atmospheric)
Notes: Example Problem on Ideal Gas Law

## Slide 13: Pressure

## Slide 14: Sample Problems – Ideal Gases
A lab is conducting experiments. The temperature is 27oC and the pressure is 14 psi. What is the density of the air?
Express you answers in both slugs/ft3 and kg/m3
What happens if we conduct the same experiment at an altitude of 30000 feet. What are typical temperatures and pressures at that height. What will the density of air be up there?

## Slide 15: Viscosity
Viscosity is a measure of a fluid’s resistance to shear – more viscous, more resistance
Intrinsic property of a fluid (varies with temperature)
Viscosity causes fluids to adhere to solid boundaries https://www.youtube.com/watch?v=V5a4kP-5Jiw
Observations show shear stress is proportional to velocity gradient
(Dynamic) Viscosity (m) is the constant or proportionality s.t.
Kinematic Viscosity (n=m/r) is also commonly used in formulas.
What’s more viscous: Water or Air??
Notes: Discussion on what fluids are more viscou that others?
Differences between kinematic and dynamic

## Slide 16: Velocity profile of air over a car roof
Where is the region of maximum shear stress?

## Slide 17: Sample Problem – Shear Stress due to viscosity
You measure a velocity profile for water at 15.6oC in the lab that can be fit with the polynomial
Calculate an expression for the shear stress? Plot it.
Where is it maximum? What is the value?
Where is it minimum? What is the value?

## Slide 18: Compressibility
How much does the volume of a fluid change for a given change in pressure
Bulk Modulus
How is this different for gases and fluids?

## Slide 19: Compression of Gases
Two common approaches are used
        Isothermal (constant temperature) so from ideal gas law
        Isentropic (no change in entropy, frictionless with no exchange of heat to surroundings)
For many gases k ~ 1.4
See table B3 and B4 in text

## Slide 20: Speed of Sound
What is the speed of sound?
https://www.youtube.com/watch?v=OEmiTYtW5cs
https://www.youtube.com/watch?v=PQydRIxoAU0

## Slide 21: Speed of Sound
What is the speed of sound?
  A measure of how quickly small disturbances propagate
What does this mean for speed
of sound in a liquid relative to a
gas?

## Slide 22: Sample Problem – Speed of Sound in Water vs. Air
Which do you think is greater?
Calculate them…..

## Slide 23: Surface Tension
Surface tension is a property of fluid that is important at interfaces between different fluids. The different molecular dynamics on each side of the interface lead to surface tension
How insects walk on water; how droplets form in a specific shape
Sensitive to changes in chemical composition (i.e. you can change surface tension easily by dissolving a solute in a fluid)
For a capillary rise
Notes: Derive on blackboard

## Slide 24: Capillary Rise

## Slide 25: Sample Question – Walking on Water…
A water strider is supported on the surface of a pond by surface tension acting along the interface between the water and the bugs’ legs. Determine the minimum length of the interface needed to support the bug
Assume the bug weighs 10-4 N and that surface tension acts only vertically upwards
Repeat the calculation for an average human weighing 750N

## Slide 26: Important Equations
Specific Weight g=rg
Ideal Gas Law p=rRT
Newtonian Fluid Shear Stress t=m du/dy
Bulk Modulus
Speed of Sound
Capillary Rise in a Tube