## Slide 1: Review Session 1

## Slide 2: Events during Precipitation - Infiltration
Not all water that falls will reach the water table
Infiltration Capacity is measure of a soils capacity to absorb water
Highly variable – soil type, but also the same soil varies depending on current moisture content
Horton Infiltration Capacity Equation

## Slide 3: Example
Consider the following rain event
  25mm/hr for 1st hour
  50 mm/hr during 2nd hour
  10 mm/hr for 3rd hour
  How much infiltration will happen into a soil with the following Horton infiltration capacity parameters
  fc=20 mm/hr
  fo=80 mm/hr
  k=3/4

## Slide 4: Plot Precipitation and Infiltration Capacity against time

## Slide 5: Find minimum across each interval

## Slide 6: Perform Calculation

## Slide 7: Streams and Groundwater Gaining vs Losing
How do you determine which it is? – Groups

## Slide 8: Stream Hydrographs – Baseflow Recessions
Baseflow is is the portion of streamflow that comes from subsurface flow
Baseflow recession in a stream occurs when groundwater feed to a stream decreases

## Slide 9: Stream Hydrographs – Baseflow Recessions
Complex thing that depends on lots of characteristics in a watershed (topography, drainage, soils +geology)… but often the equation is simple
a is a constant for a given river and will not change from year to year unless there has been some dramatic events that have changed the local hydrology
(same goes for t1, which is an indirect measure of a, in the following examples)

## Slide 10: Determining Ground-Water Recharge from Baseflow
Seasonal Recession Method
Find time t1 when Q=Q0/10
Find Vtp, the volume of potential gw discharge
Calculate potential baseflow at t, the end of the recession
Recharge= Vtp(next season)- Vt(season 1)
Apply algorithm to this figure

## Slide 11: Example
Compute the volume of annual recharge that occurs between runoff year 1 and 2

## Slide 12: Step a - Find time t1 when Q=Q0/10
Q0(1)=3000
Q0(1)=3000
Q0(1)/10=300
t1
t1=(6-2)=4

## Slide 13: Step a - Find time t1 when Q=Q0/10
Q0(1)=3000 m3/s
t1=4 months
t1

## Slide 14: Step a - Find time t1 when Q=Q0/10
Q0(2)=4000 m3/s
Q0(2)=4000 m3/s
t1

## Slide 15: (c) Calculate potential baseflow at t, the end of the recession
t
t=(10-2)=8 months
t1

## Slide 16: Final step calculate recharge
Recharge= Vtp(next season)- Vt(season 1)

## Slide 17: Determining Ground-Water Recharge from Baseflow
Recession Curve Displacement
Find t1
Compute tc=0.2144t1
Locate time tc after peak
Extrapolate recession A and B to find QA and QB at tc
Apply equation

## Slide 18: Example
Q (m3/s)

## Slide 19: Step 1 – find t1
Extrapolate lower curve out over all times
Pick any point on this curve
Q0=20 on day 3
Q0/10=2
t1
t1=62-3=59 days
Q (m3/s)

## Slide 20: Step 2 – Compute tc=0.2144t1
Extrapolate lower curve out over all times
Q0=20 on day 2
Q0/10=2
t1
t1=62-3=59 days
tc=0.2144t1=12.5 days
Q (m3/s)

## Slide 21: Step 3 – Locate time tc after peak
Extrapolate lower curve out over all times
Q0=20 on day 2
Q0/10=2
t1
t1=62-3=59 days
tc=0.2144t1=12.5 days
tc
Q (m3/s)

## Slide 22: Step 4 – Extrapolate recession A and B to find QA and QB at tc
Extrapolate lower curve out over all times
Q0=20 on day 2
Q0/10=2
t1
t1=62-3=59 days
tc=0.2144t1=12.5 days
tc
QB=30m3/s
QA=9m3/s
Q (m3/s)

## Slide 23: Calculate Recharge
t1=59 days
QB=30m3/s
QA=9m3/s

## Slide 24: Open Channel Flow – Manning Equation
Imperial Units
V (ft/s)– average velocity
R (ft)- hydraulic radius (ratio of cross area to wetted perimeter)
S (ft/ft) - energy gradient
n – Manning roughness coefficient
Metric Units
V (m/s)– average velocity
R (m)- hydraulic radius (ratio of cross area to wetted perimeter)
S (m/m) - energy gradient
n – Manning roughness coefficient
a
b

## Slide 25: Manning Roughness Coefficient
Stream Type | n
Mountain stream with rocky bed | 0.04-0.05
Winding Natural Stream with weeds | 0.035
Natural stream with little vegetation | 0.025
Straight, unlined earth channel | 0.02
Smoothed concrete | 0.01
Entirely empirical so be very careful with units!!!

## Slide 26: Useful Definitions
Confining Layer – geologic unit with little or no intrinsic permeability
Aquifuge – Absolutely impermeable unit that will not transfer water
Aquitard – a layer of low permeability that can store ground water and transmit it slowly from one aquifer to another
Unconfined/Confined Aquifer – an aquifer without/with a confining layer on top.
Leaky Confined Aquifer – a confined aquifer with an aquitard as one of its boundaries
Perched Aquifer – a layer of saturated water that forms due to accumulation above an impermeable lens (e.g. clay)
Water Table – depth where the soil becomes completely saturated

## Slide 27: Porosity
Porosity is the ratio of the volume of voids to the total volume
0<n<1, although sometimes we express it as a percentage by multiplying by 100
Question: How would you measure this?

## Slide 28: What does porosity depend on
Packing
Cubic/Hexagonal/Rhombohedral Packing – Calculate the porosity….
Cubic vs Hexagonal vs Rhombohedral
(47.65%) (39.5%) (25.95%)

## Slide 29: What does porosity depend on
Porosity depends on Packing
Porosity DOES NOT depend on the size of the grains!!!

## Slide 30: Grain Size Distribution
Very few materials have uniform grain sizes.
In order to measure the distribution of grains successively sieve materials through sieves of different size and build grain size distribution
Metrics – d10 and d60 (ten and sixty percentile diameters)
CU=d60/d10 – coeff of uniformity
CU<4 well sorted
CU>6 poorly sorted
d10 is called effective grain size

## Slide 31: Typical GSD
GSD of silty fine to medium sand – What is CU
d60
d10
Cu=d60/d10 (must be >1)

## Slide 32: Specific Yield
Specific yield (Sy) is the ratio of the volume of water that drains from a saturated rock owing to the attraction of gravity to the total volume of the saturated aquifer.
Specific retention (Sr) is the rest of the water that is retained
Question: You have two materials with cubic packing; one is made up of small spheres, the other of larger ones; which has the larger specific retention? Think about the physics of what is retaining the water?

## Slide 33: Hydraulic Conductivity
Measure flowrate Q to estimate specific discharge (velocity)
q=Q/Area
Observations

## Slide 34: Darcy’s Law
Hydraulic Conductivity
Hydraulic Conductivity depends on both the
fluid and the porous medium

## Slide 35: Further Observations
In a bed of packed beads the flow rate is proportional to the diameter squared
The flow rate is proportional to the specific weight of the fluid
The flow rate is inversely proportional to the viscosity of the fluid

## Slide 36: Therefore
Property of the porous medium
only called intrinsic permeability
Denoted ki with units m2 (or Darcy’s)
1 Darcy=1x10-8cm2
Property of the fluid only
What drives the flow

## Slide 37: Hazen Formula for Hydraulic Conductivity
Effective diameter d10
Hazen proposed that hydraulic conductivity is given by
K=C (d10)2
This is for water!!!!
C – shape factor (see adjacent table)
d10 in cm
K is given in cm/s
C shape factor
Very fine sand: C=40-80
Fine sand: C=40-80
Medium sand: C=80-120
Coarse sand: C=80-120 (poorly sorted)
Coarse sand: C=120-50 (well sorted, clean)

## Slide 38: How to Measure Permeability
Measure Volume V over time t
Hydraulic Conductivity is given by

## Slide 39: Transmissivity
We like to think about groundwater in 2-dimensions (like a map).
Therefore we like to define the permeability over the depth of the aquifer (depth b)
Tranmissivity
T=bK

## Slide 40: More Generally
N parallel layers, each with conductivity Ki of thickness bi
N perpendicular to flow layers, each with conductivity Ki of thickness bi
K1
K2
K3
KN
K1
K2
K3
K4

## Slide 41: Formally
Darcy’s Law
where
q is a vector
K is a symmetric tensor (matrix) Kxy=Kyx
is a vector

## Slide 42: Hydraulic Gradient and Potentiometric Surface
3 well setup
Draw lines connecting wells
Note elevation at each well
Map distances between wells
Note difference in elevations
Find distance for unit head drop between wells
Mark even increments
Repeat for all well pairs
Create Contour Lines
Gradient normal to these lines

## Slide 43: Steady Flow in Confined Aquifer

## Slide 44: Steady Flow in an Unconfined A quifer

## Slide 45: What about 2-d steady state
Confined
Unconfined
Direction of Flow (for both cases)
qy
qx
q
Recall that there are two angles that satisfy this equation. You must pick the correct one!

## Slide 46: Groundwater Divides
Location of GW Divide is where q’=0

## Slide 47: Final Test
If you were to compare the water levels in wells A and B, which well would have the higher water level?
How would you calculate the water level difference between A and B?
Which well has the higher water level, well A or Well Q?