## Slide 1: Review 1

## Slide 2: Solve These Two Differential Equations
I expect you to be able to Solve the following differential equations with Boundary conditions

## Slide 3: Control Volume
Recall the idea of a Control Volume - Consider an arbitrary volume of your choosing and write an equation for conservation of mass for it
This is the most fundamental and important law for anything relating to transport of contaminants
Change in Mass
=
Amount of Mass Flowing in – Amount of Mass Flowing out
Rate of change of Mass
in Control Volume
Mass flow rate in
(sum of all in)
Mass flow rate out
(sum of all in)

## Slide 4: What if we consider an infinitessimal control volume?
Start in 1d (as in nothing can flow in y and z)
Dx
Dy
Dz
What is the flux j?

## Slide 5: Basics on Contaminant Transport
What processes do we usually consider?
Advection – the solute simply moves with the velocity of the surrounding fluid

## Slide 6: Basics on Contaminant Transport
What processes do we usually consider?
Diffusion – Because molecules bounce around randomly and off one another they also spread randomly (usually a slow process)
Cause solute to dilute, because it spreads over a greater area/volume

## Slide 7: Quiz
A room is 10 meters long. The coefficient of molecular diffusion is 10-9 m2/s. If something is released in the room how long does it take diffusion to spread it throughout the whole space.
What if it is 0.1, 1 or 100 meters long?

## Slide 8: 1d ->The Fundamental Solution
Solution
Mass of solute injected

## Slide 9: 3 important properties
Peak Concentration
Center of the Plume
Characteristic Width of the Plume

## Slide 10: Spatial Moments
Moment
Zeroth Moment
First Moment
Second Moment
Second Centered Moment (k11=m2-m12)

## Slide 11: Spatial Moments
Zeroth Moment – 1 (normalized total mass)
First Moment – vt (center of mass)
Second Moment – 2Dt+v2t2 (measure of weight of plume relative to a reference point)
Second Centered Moment - 2Dt (a measure of the width of the plume that increases due to dispersion)

## Slide 12: Temporal Moments of Breakthrough Curves
Another popular method is to look at temporal moments of breakthrough curves (i.e. you have a concentration measurement at a fixed distance x and integrate over time)
It is often easier to measure breakthrough curves than spatial distribution of solutes and this information can also be used to infer parameters (such as v and D in the ADE).

## Slide 13: Evaluating these for ADE
For

## Slide 14: Linear Superposition
Imagine you have two spills
Concentration in your domain is always

## Slide 15: Different Condition 1:Step Condition
Heaviside Step Function
H(y) =1 if y>0
=0 if y<0
Concentration behind x=x0
Is C0 and ahead of it zero
If you need to calculate erfc(x) you will get a table like this one

## Slide 16: Different Condition 2: Wide Pulse Condition
Heaviside Step Function
Concentration between
x1<x<x0 is C0
Elsewhere is 0

## Slide 17: What Does Flow in a Stream/River Look Like?
Flow is Three Dimensional with important features in each direction: x (in direction of flow), y (transverse to flow) and z (vertical).
x,y (overhead view)
x
y
Turbulent – almost plug flow
At boundary is zero
Typically we treat as uniform
River Banks
x,z (side view)
Log Profile increasing
toward free surface
Free Surface
River Bed
H
W

## Slide 18: DownsTream Transport
If I am only interested in downstream transport, surely I should only need a one-dimensional transport equation like:
Under what conditions can I do this? – i.e. look at the previous slide equation. What has to be true for the equation to collapse to the above one?
When vertical and Transverse Directions are Well Mixed dx

## Slide 19: Well Mixed Transverse to Flow
You can assume that vertical gradients are negligible after
Likewise transverse gradients are negligible after
Therefore at least one of these times must have passed before you can treat the system as one dimensional

## Slide 20: Log Law
x,z (side view)
Log Profile increasing
toward free surface
Free Surface
River Bed
H
Von Karman constant
Roughness Height
Friction Velocity
S – Energy Gradient

## Slide 21: Dispersion
People like Fisher and GI Taylor produced an elegant formula for longitudinal dispersion. It is rigorous, but the derivation of it is cumbersome (if you’re interested take my advanced grad class).

## Slide 22: SO
Once
Then

## Slide 23: Also
I know the time when I can apply Taylor dispersion (i.e. assume transport is one-dimensional) – how far from a point spill must I be to be able to apply it?

## Slide 24: First oRder REaction
The solution to
Is
In general if you know answer for conservative, multiply by decaying exponential like this!!
The total amount of mass in your system is decaying exponentially over time

## Slide 25: If we include both advection and dispersion
Imagine you have a continuous source at x=0 and you are only interested in x greater than zero (semi-infinite domain)
The general solution to this ODE is
A1=0, because concentration must be finite as x->infinity

## Slide 26: Mathematical Model
Based on our conceptual figure and ideas
Transport is by vertical dispersion…
Light
H
Constant Concentration Bottom Boundary

## Slide 27: What about reaction
Assume zeroth order (often assume first order, but maths gets complicated and I want to focus on general idea first – we will look at complicated maths next):
i.e. does not depend on C – what does this mean?
Light attenuation means light intensity decays exponentially with depth in water
How about:

## Slide 28: Therefore
Do you see a problem with this solution?
Zeroth order approximation only good in certain circumstances – what are they?

## Slide 29: Compartmental Models
Lakes are often modeled as different sections, each of which are well mixed, e.g.
Layer 1
Layer 2
Layer 3
Evap
Precip
Swout,1
Swin,1
Gwin,1
Gwin,2
Gwout,3
Gwout,2
Gwout,2
Gwin,3
Exchange12
Exchange23
Write a Mass Balance Equation For Each Layer!
RXN1
RXN2
RXN3
We can as many layers as we want

## Slide 30: Mass Balance – No RXNs
Layer 1
Layer 2
Layer 3

## Slide 31: How can we simplify?
Assume Well Mixed- any concentration leaving a layer is the concentration of that layer.
Assume the volume of each layer is fixed
Assume exchange between layers is perfectly balanced (e.g. Q1,2=Q2,1) – can you justify this? What does it mean?
Precipitation and Evaporation Balance; Groundwater Input and Outputs Balance; Surface Water Inputs and Outputs Balance - Is this reasonable?
Precipitation and Evaporation carry negligible loads (when might this be a bad assumption – think of an example??)
All GW is equally loaded with whatever substance you’re interested in

## Slide 32: Mass Balance – No RXNs
Layer 1
Layer 2
Layer 3

## Slide 33: Particle Settling
Weight
Drag
Buoyancy

## Slide 34: Particle Settling Velocity
Weight
Drag
Buoyancy
Proportional
to radius
squared
I expect you to know this (not just the last part)

## Slide 35: Vertical Distribution of Particles in a Water Body
Vertical dispersion tries to mix particles vertically in a water column
Gravity is trying to pull them down
At equilibrium these balance

## Slide 36: Power Law Fit
Y=aXb

## Slide 37: Example Problem
Data is online
Open Matlab
Empirical_Example.m
Tonnes per day

## Slide 38: Example Problem Continued
Tonnes per day
Tonnes per month
Tonnes

## Slide 39: Air-water Exchange
Cair
Cwater
Gas exchange coefficient
What is it?
What does it depend on?